## Slide 1: AIML for Robotics
Module 3
Localization
Section Faculty:
Dr. Sangeetha Viswanathan

## Slide 2: The course owner and the authors of this course deck, Prof. Raja vadhana and Dr.Sangeetha, are gratefully acknowledging all authors who made their course materials freely available online.

## Slide 3: Course Content
Introduction
  Types of Robots
  Mobile Robots – Use case of Programmable solutions
Components of Programmable Robotic System
  Perception
  Representation
  Motion
Localization
  Taxonomy
  Types
Mapping
  Feature Based
  Grid Based
Path Planning
  Graph Based
  Sample Based
  Evolutional Techniques
Human – Robot Interaction
  Ethics
  Introduction to Visual Bot
  Introduction to Chat Bot

## Slide 4
Today's Roadmap
01
What is a map frame?
Global vs robot frame, and the translate + rotate math that bridges them.
02
Where does localization show up?
Mobile robots (Roomba, AMR, Mars rover) and software agents (cyber bots, RPA, crawlers).
03
What kind of localization problem is it?
A four-axis taxonomy: static/dynamic, single/multi, local/global, passive/active.
04
How does grid-based localization work?
The histogram filter end-to-end: predict step (motion) and update step (measurement).
05
Where does AI/ML fit?
Noisy sensors, learned models, action recommendation. And when to switch to Monte Carlo.

## Slide 5
The Big Question
“Where am I?”
Every autonomous system — physical or digital — must answer this repeatedly, in real time, from noisy and incomplete information.
PERCEPTION
Perception
Sense the world — LIDAR, camera, packet, log.
LOCALIZATION
Localization
Convert sensing into a belief about state.
← We are here
ACTION
Action / Planning
Decide what to do given that belief.

## Slide 6: Map Frame

## Slide 7: Frame
X=2,Y=3
X=4,Y=5
Global Map Frame
Range(r, o) = ~3.16 meters

## Slide 8
The Global Map Frame
A fixed origin and axes everyone in the system agrees on
All landmarks, walls, and the robot's pose are expressed in one fixed coordinate system.
Robot pose: (2, 3), θ = 45°
Landmark: (4, 5)
Range: √8 ≈ 2.83 m
KEY IDEA
The map frame is fixed. It does not know or care where the robot is — it is the reference the robot localizes against.
Origin is picked at map-creation time (a warehouse corner, a lat-lon, etc.).
X
Y
Robot (2,3,45°)
Landmark (4,5)

## Slide 9
The Local Robot Frame
The robot's own system — origin at itself, x-axis along its heading
Everything the robot does — “move forward 1 m”, “scan at +30°”, “wall on my left” — is naturally expressed in this frame.
GLOBAL MAP FRAME
What the map says
Robot at (2, 3), θ = 45°
Landmark at (4, 5)
Origin = fixed point on the map
Axes along map north / east
The robot is one object among many here.
LOCAL ROBOT FRAME
What the robot sees
Robot at the origin (0, 0)
x'-axis = direction it faces
y'-axis = 90° to the left
Landmark = (2.83, 0) straight ahead
Same landmark, two valid coordinates.

## Slide 10: Frame
X=2,
Y=3,
Θ = 45
X=4,Y=5
X=2,
Y=3,
Θ = 45
Local Robot Frame
Translate map point to robot frame
Rotate coordinates by –θ
Rot(
Rot(

## Slide 11: Frame
X=2,
Y=3,
Θ = 45
X=4,Y=5
X=2,
Y=3,
Θ = 45
Local Robot Frame
Translate map point to robot frame
Rotate coordinates by –θ
Rot(
Rot(

## Slide 12: Frame
X=4,Y=5
X=2,
Y=3,
Θ = 45
Local Robot Frame
Translate map point to robot frame
Rotate coordinates by –θ
Rot(
Rot(

## Slide 13: Frame
X=4,Y=5
X=2,
Y=3,
Θ = 45
Local Robot Frame
Translate map point to robot frame
Rotate coordinates by –θ
Rot(
Rot(

## Slide 14: Frame
X=4,Y=5
X=2,
Y=3,
Θ = 45
Local Robot Frame
Rot(
Rot(

## Slide 15: Frame
X=4,Y=5
X=2,
Y=3,
Θ = 45
Rot(
Rot(
Local Robot Frame
Rotate coordinates by +θ

## Slide 16: Frame
X=4,Y=5
X=2,
Y=3,
Θ = 45
Rot(
Rot(
Local Robot Frame
Rotate coordinates by +θ
Translate robot to map frame

## Slide 18: Robot Localization
Sensor Data : Z t

## Slide 19
Robot Localization — Formally
A continuous estimation problem, not a one-shot fix
DEFINITION
Localization is the problem of maintaining a probability distribution over the robot's pose, given a map, a sequence of control inputs, and a sequence of sensor measurements.
Inputs
Map (m)
World model — 2D grid, point cloud, topological graph.
Controls (u₁:t)
Control inputs — wheel velocities, steering, accelerations.
Measurements (z₁:t)
Sensor readings — LIDAR, camera, IMU, GPS.
Bayes filter
predict + update
Output
bel(xₜ)
Belief — a probability distribution over all possible poses at time t.
Not a single number — a distribution. “I'm 70% sure I'm here, 25% over there, 5% scattered.”

## Slide 20
Use Cases — Mobile Robots
State = (x, y, θ). Sensors = LIDAR, camera, IMU, odometry, GPS.
Warehouse AMR
Finds itself in the pallet aisle.
Roomba / vacuum
Knows which rooms it cleaned.
Self-driving car
Lane-level pose vs HD map.
Mars rover
Visual-inertial pose, no GPS.
Delivery drone
Geo-pose for last-100m landing.
Surgical robot
Tool-tip pose vs anatomy.

## Slide 21
Use Cases — Software Agents
State = (host, subnet, privilege). “Sensors” = packets, syscalls, logs.
Pen-test bot
Locates itself in the net graph.
you are here
Threat-hunter
Pinpoints attacker's stage.
Recon
Foot
Lateral
Exfil
attacker is here
SOAR bot
Finds the kill-chain stage.
← step?
Web crawler
Its position in the site graph.
/
/a
/blog
/c
crawler is here
RPA bot
Its place in a workflow.
step 3 of 4
Game NPC
Pose in a virtual world.

## Slide 22
The Shared Bayes-Filter Pattern
Physical or digital, the math is the same — only the state changes
THE BAYES-FILTER PATTERN
bel(xₜ) = η · p(zₜ | xₜ) · ∫ p(xₜ | uₜ, xₜ₋₁) · bel(xₜ₋₁) dxₜ₋₁
Predict (motion) → Update (measurement) → Normalize → Loop.
Component
Physical (mobile robot)
Logical (software agent)
State (xₜ)
Pose: (x, y, θ)
Network position: (host, subnet, privilege)
Action (uₜ)
Move forward 1 m, turn 30°
scp file, sudo, click button
Sensor (zₜ)
LIDAR ranges, image, IMU
Packet capture, log line, API response
Goal
Reach pose (xg, yg)
Reach asset (DB server, admin shell)
“Where am I?” is the same question. The substrate changes; the algorithm doesn't.

## Slide 23: Taxonomy of Localization Problems
Problem Types
Static vs Dynamic
Environment
Single vs multiple
Agent/s
Local vs Global
Knowledge
Passive vs Active
Motion Control
Varying Features of the Environment
Knowledge of Initial Pose
Level of Uncertainty
Recovery from Failures : Kidnapped Robot Problem
Necessity for Real time Control

## Slide 24
Four Axes of Localization Problems
Pick a side on each axis — the combination tells you which algorithm applies
Environment
STATIC
Walls and landmarks don't move.
vs
DYNAMIC
People, vehicles, objects move.
Agents
SINGLE
One robot, one belief.
vs
MULTIPLE
Robots share or compete for a map.
Knowledge
LOCAL (tracking)
We know roughly where we started.
vs
GLOBAL (kidnapped)
No initial pose — could be anywhere.
Motion Control
PASSIVE
Localize from whatever motion happens.
vs
ACTIVE
Move on purpose to cut uncertainty.
Example: a Roomba in a quiet room is STATIC · SINGLE · LOCAL · PASSIVE → textbook grid filter works.

## Slide 25
Axis 1 — Static vs Dynamic Environment
Does anything in the map move while the robot localizes?
STATIC
Map features don't change
Walls, landmarks and obstacles are fixed across the localization window.
EXAMPLES
Roomba in an empty room
Warehouse AMR after hours
Mars rover (Mars doesn't move)
DYNAMIC
Features change over time
People walk through, vehicles move, the attacker pivots between hosts.
EXAMPLES
Self-driving car in traffic
Service robot in an airport
Threat-hunter chasing a target

## Slide 26
Axis 2 — Single vs Multiple Agents
Are we localizing one entity, or many that can share information?
SINGLE AGENT
One robot, one belief
All information comes from this robot's own sensors and motion history.
EXAMPLES
Single Roomba in a house
Solo Mars rover
One pen-test bot on a target
MULTIPLE AGENTS
Several robots, shared map
Robots observe each other and share beliefs — cooperative localization.
EXAMPLES
Warehouse fleet (Amazon, Ocado)
Drone swarm in search & rescue
Connected vehicles (V2V)
WHY HARDER
Joint belief grows exponentially with the number of agents — needs decentralized algorithms.

## Slide 27
Axis 3 — Local vs Global Knowledge
How well do we know the initial pose? Can we recover if moved?
LOCAL (tracking)
We know where we started
Belief is a tight unimodal distribution; the filter tracks small corrections.
EXAMPLES
Roomba returning to dock
Lane keeping in a car
Arm tracking from a zero
GLOBAL (kidnapped)
Could be anywhere
Belief starts uniform — every cell equally likely; converge from scratch.
EXAMPLES
Roomba just turned on
Robot picked up and moved
Bot dropped in unknown subnet
KIDNAPPED-ROBOT PROBLEM
A confident robot is teleported. Grid filters keep mass everywhere and can recover; pure Kalman filters collapse to one mode and stay wrong.

## Slide 28
Axis 4 — Passive vs Active Localization
Do we choose motions to help ourselves localize?
PASSIVE
Localize from whatever happens
Motion is dictated by the task; the filter just reads u and z.
EXAMPLES
Roomba runs its clean pattern
Car drives the chosen route
Crawler follows existing links
ACTIVE
Move to reduce uncertainty
Pick the action with the most expected information gain — go disambiguate.
EXAMPLES
Drive to a corner to break symmetry
Rover picks informative viewpoint
Active scanning to ID the OS
WHERE RL SHINES
Active localization learns a policy that minimises belief entropy — a major entry point for reinforcement learning.

## Slide 29
Where AI/ML Lives Inside Localization
Five entry points into the classical Bayes pipeline
Component
Why classical struggles
Where AI/ML helps
Motion model p(xₜ|uₜ,xₜ₋₁)
Wheels slip, terrain varies.
Learn noise from telemetry (GP regression).
Measurement model p(zₜ|xₜ)
Sensor responses non-Gaussian.
Neural likelihood — CNN(image, pose) → score.
Map representation
Hand-built maps go stale.
Learned features (SuperPoint); NeRF / occupancy fields.
State estimator itself
Real distributions are weird.
DeepKF / deep variational filters learn the update.
Active control policy
Hand-tuned heuristics fall short.
RL — reward = information gain.
ML wins where the analytical model breaks down — unmodellable terrain, non-Gaussian sensors.

## Slide 30: Discrete Bayes Filters

## Slide 31: Recursive State Estimation Bayes Filter Algorithm
Initial Belief
Control Update
Measurement Update
X0 | P(X0)
is_open | 0.5
Is_closed | 0.5
Xt-1 | Ut | P(Xt =is_open) | P(Xt =is_closed)
is_open | push | 1 | 0
Is_closed | Push | 0.8 | 0.2
is_open | do_nothing | 1 | 0
Is_closed | do_nothing | 0 | 1
Xt | P(Zt = sense_open) | P(Zt = sense_closed)
is_open | 0.6 | 0.4
Is_closed | 0.2 | 0.8

## Slide 32: Grid Based Localization Histogram Filter Approach

## Slide 34: Grid Based Localization Histogram Filter Approach
X=5 | X=10 | X=15 | X=20
X0 | P(X0)
5 | 0.25
10 | 0.25
15 | 0.25
20 | 0.25
Xt | P(Zt =5) | P(Zt =10) | P(Zt =15) | P(Zt =20)
5 | 0.8 | 0.1 | 0.1 | 0
10 | 0.3 | 0.4 | 0.2 | 0.1
15 | 0.1 | 0.2 | 0.4 | 0.3
20 | 0 | 0.1 | 0.1 | 0.8

## Slide 35: Grid Based Localization Histogram Filter Approach
X=5 | X=10 | X=15 | X=20
X0 | P(X0)
5 | 0.25
10 | 0.25
15 | 0.25
20 | 0.25
Xt | P(Zt =15)
5 | 0.1
10 | 0.2
15 | 0.4
20 | 0.1
Predict Step:
(Motion)
Update Step:
(Measurement)
Xt-1 | Ut | P(Xt =5) | P(Xt =10) | P(Xt =15) | P(Xt =20)
5 |  | 0.2 | 0.6 | 0.2 | 0
10 |  | 0.3 | 0.1 | 0.6 | 0.1
15 |  | 0.1 | 0.3 | 0.1 | 0.5
20 |  | 0 | 0.1 | 0.3 | 0.6

## Slide 36: Grid Based Localization Histogram Filter Approach
X=5 | X=10 | X=15 | X=20
X0 | P(X0)
5 | 0.25
10 | 0.25
15 | 0.25
20 | 0.25
Xt | P(Zt =15)
5 | 0.1
10 | 0.2
15 | 0.4
20 | 0.1
Predict Step:
Xt-1 | Ut | P(Xt =5) | P(Xt =10) | P(Xt =15) | P(Xt =20)
5 |  | 0.2 | 0.6 | 0.2 | 0
10 |  | 0.3 | 0.1 | 0.6 | 0.1
15 |  | 0.1 | 0.3 | 0.1 | 0.5
20 |  | 0 | 0.1 | 0.3 | 0.6

## Slide 37: Grid Based Localization Histogram Filter Approach
X=5 | X=10 | X=15 | X=20
X0 | P(X0)
5 | 0.25
10 | 0.25
15 | 0.25
20 | 0.25
Xt | P(Zt =15)
5 | 0.1
10 | 0.2
15 | 0.4
20 | 0.1
Predict Step:
Xt-1 | Ut | P(Xt =5) | P(Xt =10) | P(Xt =15) | P(Xt =20)
* |  | 0.15 | 0.275 | 0.3 | 0.3

## Slide 38: Grid Based Localization Histogram Filter Approach
X=5 | X=10 | X=15 | X=20
X0 | P(X0)
5 | 0.25
10 | 0.25
15 | 0.25
20 | 0.25
Xt | P(Zt =15)
5 | 0.1
10 | 0.2
15 | 0.4
20 | 0.1
Update Step:
Xt-1 | Ut | P(Xt =5) | P(Xt =10) | P(Xt =15) | P(Xt =20)
* |  | 0.15 | 0.275 | 0.3 | 0.3
 |  | 0.015 | 0.055 | 0.12 | 0.03
 |  | 0.06 | 0.25 | 0.55 | 0.14

## Slide 41: Grid Based Localization Histogram Filter Approach

## Slide 42: Grid Based Localization : Piecewise Constant Approximation
Accuracy Vs Resource Intensive

## Slide 43: Grid Based Localization : Optimization Techniques
Fine Grained Representation with fixed Grid Structures

## Slide 44: Grid Based Localization : Optimization Techniques
Fine Grained Representation with fixed Grid Structures

## Slide 45: AIML in Grid Localization :
Use Cases:
Multiple Sensor Input are available . Measurement Models are noisy.
Image Captured from camera as streams
Recommend Actions for localization

## Slide 46: Grid Based Localization : Optimization Techniques
Fine Grained Representation with fixed Grid Structures
Pre-caching
Sensor Sub Sampling
Delayed Motion Updates
Selective Updating
Heuristics

## Slide 47: Grid Based Localization : Optimization Techniques
Coarse Grained Representation with Dynamic Grid Structures
Topological Representation
Inflate Motion Noise
Inflate Measurement Noise

## Slide 48: Grid Based Localization : Optimization Techniques
Coarse Grained Representation with Dynamic Grid Structures
Topological Representation
Inflate Motion Noise
Inflate Measurement Noise
1m Grid
Robot moves right to 0.2m from x=0
Landmark at 3m
G=0 (0,0) | G=1 | G=2 | G=3
Time | Pose | Grid | Bel(0) | Bel(1) | 
0 | 0.0 | 0 | 1.0 | 0 | 
1 | 0.2 | 0 | 1.0 | 0 | 
2 | 0.4 | 0 | 1.0 | 0 | 
3 | 0.6 | 0 | 1.0 | 0 | 
4 | 0.8 | 0 | 1.0 | 0 | 
5 | 1.0 | 1 | 0 | 1.0 | 

## Slide 49: Grid Based Localization : Optimization Techniques
Coarse Grained Representation with Dynamic Grid Structures
Topological Representation
Inflate Motion Noise
Inflate Measurement Noise
1m Grid
Robot moves right to 0.2m from x=0
Landmark at 3m
G=0 (0,0) | G=1 | G=2 | G=3
Time | Pose | Grid | Bel(0) | Bel(1) | 
0 | 0.0 | 0 | 1.0 | 0 | 
1 | 0.2 | 0 | 0.8 | 0.2 | 
2 | 0.4 | 0 | 0.64 | 0.36 | 
3 | 0.6 | 0 | 0.512 | 0.488 | 
4 | 0.8 | 0 | 0.41 | 0.59 | 
5 | 1.0 | 1 | 0.33 | 0.67 | 
Add Noise to Motion by adding small probability proportional to movement / cellSize = 20%

## Slide 50: Grid Based Localization : Optimization Techniques
Coarse Grained Representation with Dynamic Grid Structures
Topological Representation
Inflate Motion Noise
Inflate Measurement Noise
1m Grid
At t=2, Robot is at 0.4m and senses landmark at 2.6m
Keep sensor noise = 0.1
Landmark at 3m= Mean
G=0 (0,0) | G=1 | G=2 | G=3
Add Noise to Motion Model Eg., 0.5
P(Z | X) = 0.0003 (Apply Gaussian Dist)
Inference :
Most likely the robot is not in Grid 0 !!!!
P(Z | X) = 0.73 (Apply Gaussian Dist)
Inference :
Most likely the robot is not in Grid 0 !!!!
Grid | Mean | P(Z¦X)0.1 | P(Z¦X) 0.5
0 | 3m | 0.003 | 0.73
1 | 2m | ~0 | 0.37
2 | 1m | ~0 | 0.03

## Slide 51: Grid Based Localization : Illustration
Set up 1:
15 centimeter and an angular resolution of 5 degrees
Two Laser Finders
Bean Sensor Model
Subsampling

## Slide 52: Grid Based Localization : Illustration

## Slide 53: Grid Based Localization : Illustration

## Slide 54
AI/ML in Grid-Based Localization, Specifically
Four very concrete places it pays off
01
Fusing many noisy sensors
LIDAR + camera + IMU + WiFi together: train a net mapping (cell, raw packet) → likelihood, plug into the histogram update.
USE CASE → multi-sensor mobile robot
02
Camera streams as measurements
A frame is too high-dim for an analytical likelihood. A CNN outputs a heatmap over cells — that heatmap IS p(zₜ|xₜ).
USE CASE → visual localization, no LIDAR
03
Action recommendation (active)
Which action maximises info gain? Classical entropy calc is slow; RL learns a policy π(u | bel) directly.
USE CASE → kidnapped-robot recovery
04
Learning the motion noise
Instead of hand-picking 20% / 50% inflation, train a model to predict per-cell noise from odometry vs ground truth.
USE CASE → AMR on slippery surfaces

## Slide 55: Required Reading T1 Chapter #4, #7, #8 T2 Chapter #6.1, #6.2
Next Class Plan
Monte Carlo Based Localization