## Slide 1: AIML for Robotics
Module 3
Localization
Section Faculty:
Raja vadhana Prabhakar

## Slide 2: The course owner and the authors of this course deck, Prof. Raja vadhana and Dr.Sangeetha, are gratefully acknowledging all authors who made their course materials freely available online.

## Slide 3: Course Content
Introduction
  Types of Robots
  Mobile Robots – Use case of Programmable solutions
Components of Programmable Robotic System
  Perception
  Representation
  Motion
Localization
  Taxonomy
  Types
Mapping
  Feature Based
  Grid Based
Path Planning
  Graph Based
  Sample Based
  Evolutional Techniques
Human – Robot Interaction
  Ethics
  Introduction to Visual Bot
  Introduction to Chat Bot

## Slide 4: Monte Carlo Based Localization Particle Filter Approach

## Slide 5: Monte Carlo Based Localization Particle Filter Approach

## Slide 6: Monte Carlo Based Localization Particle Filter Approach
Initialize
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
Initialize M Particles Pi with uniform belief
Move each Pi based on robot motion model
Compare predicted sensor reading Z expected with actual sensor reading Z measured
Optionally filter out surprising measurements
Weigh each Pi based on importance weights
Resample for particle set for next iteration based on Darwinian approach
Reset the belief of particles with equal likelihood

## Slide 7: Monte Carlo Based Localization MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | P1 | P2 | P3 | P4
 | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25

## Slide 8: Monte Carlo Based Localization MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
 | P1 | P2 | P3 | P4
 | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Inefficient form (modified for simplicity)
+
Linear Regression Model = +1

## Slide 9: Monte Carlo Based Localization MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | P1 | P2 | P3 | P4
 | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
(modified for simplicity)
Sample Calculation := ~0.14. For simplicity is assumed to be noise = 0.5. This is updated in all the upcoming slides with weight correction.

## Slide 10: Monte Carlo Based Localization MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
 | P1 | P2 | P3 | P4
 | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
(modified for simplicity)

## Slide 11: Monte Carlo Based Localization MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
Bel( | 0.8805 | 0.0013 | 0.1132 | 0.0031
 | P1 | P2 | P3 | P4
 | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
 | 0.8805 | 0.0013 | 0.1132 | 0.0031
(modified for simplicity)

## Slide 12: Monte Carlo Based Localization MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
Bel( | 0.8805 | 0.0013 | 0.1132 | 0.0031
 | P1 | P2 | P3 | P4
 | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
 | 0.8805 | 0.0013 | 0.1132 | 0.0031

## Slide 14: Monte Carlo Based Localization MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
Bel( | 0.8805 | 0.0013 | 0.1132 | 0.0031
 | P1 | P2 | P3 | P4
 | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
 | 0.8805 | 0.0013 | 0.1132 | 0.0031
Chart: Roulette wheel (Similar to GA 's parent selection)
| P1 | P2 | P3 | P4
 | 0.8805 | 0.0031 | 0.1132 | 0.0031
 | P1 | P2 | P3 | P4
 | (2,1,0) | (4,1,0) | (4,1,0) | (2,1,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | P1 | P2 | P3 | P4
 | (2,1,0) | (4,1,0) | (4,1,0) | (2,1,0)
 | 0.25 | 0.25 | 0.25 | 0.25
One Naïve Estimation Model :
Average of Particles = (3,1,0)

## Slide 15: Monte Carlo Based Localization Particle Filter Approach
Initialize
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
Initialize M Particles Pi with uniform belief
Move each Pi based on robot motion model
Compare predicted sensor reading Z expected with actual sensor reading Z measured
Optionally filter out surprising measurements
Weigh each Pi based on importance weights
Resample for particle set for next iteration based on Darwinian approach
Reset the belief of particles with equal likelihood

## Slide 16: Monte Carlo Based Localization Augmented MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m, α fast = 0.5, α slow = 0.1
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | P1 | P2 | P3 | P4
 | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
No Change

## Slide 17: Monte Carlo Based Localization Augmented MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m , α fast = 0.5, α slow = 0.1
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
 | P1 | P2 | P3 | P4
 | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
(modified for simplicity)
+
Linear Regression Model = +1
No Change

## Slide 18: Monte Carlo Based Localization Augmented MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m , α fast = 0.5, α slow = 0.1
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | P1 | P2 | P3 | P4
 | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
(modified for simplicity)
No Change

## Slide 19: Monte Carlo Based Localization Augmented MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m , α fast = 0.5, α slow = 0.1
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
 | P1 | P2 | P3 | P4
 | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
(modified for simplicity)
No Change

## Slide 20: Monte Carlo Based Localization Augmented MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m , α fast = 0.5, α slow = 0.1
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
Bel( | 0.8805 | 0.0013 | 0.1132 | 0.0031
 | P1 | P2 | P3 | P4
 | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
 | 0.8805 | 0.0013 | 0.1132 | 0.0031
(modified for simplicity)
No Change

## Slide 21: Monte Carlo Based Localization Augmented MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m , α fast = 0.5, α slow = 0.1
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
Bel( | 0.8805 | 0.0013 | 0.1132 | 0.0031
 | P1 | P2 | P3 | P4
 | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
 | 0.8805 | 0.0013 | 0.1132 | 0.0031
= = ~0.03975
= (1- α fast) +
= (1- α slow) +
= (1-0.5) (0.5)+
= ~0.27
= (1-0.1) (0.9)+
= ~0.81
= = 0.33
MAX{0, (1-0.33)} = ~0.67
Hence for M=4 number of particle selection in next round with 0.67 probability (approx. to 70 only for this slide’s example), exploration proceeds and for rest exploitation is preferred
One Naïve Estimation Model :
Average of Particles = (3,1,0)
Inference : Approx. 30% of Particles are Informative. Retain them . Need randomization for other 70% of M particles!
Note : Changes are made to illustrate both the process. Assume Short term likelihood = 0.5 instead of 0 and long term likelihood of 0.9 instead of 0.
Since initial values used in live class room discussion was not yielding the expected inference this is updated.

## Slide 22: Monte Carlo Based Localization Augmented MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m , α fast = 0.5, α slow = 0.1
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
Bel( | 0.8805 | 0.0013 | 0.1132 | 0.0031
 | P1 | P2 | P3 | P4
 | (1,1,0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (2,1,0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | 3.6 | 2.24 | 3 | 2.24
 | 0.14 | 0.0005 | 0.018 | 0.0005
 | 0.8805 | 0.0013 | 0.1132 | 0.0031
Chart: Roulette wheel (Similar to GA 's parent selection)
| P1 | P2 | P3 | P4
 | 0.8805 | 0.0031 | 0.1132 | 0.0031
 | P1 | P2 | P3 | P4
 | (2,1,0) | (4,2,0) | (0,0,0) | (6,2,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | P1 | P2 | P3 | P4
 | (2,1,0) | (4,2,0) | (0,0,0) | (6,2,0)
 | 0.25 | 0.25 | 0.25 | 0.25
One Naïve Estimation Model :
Average of Particles = (2,1,0)
Based on previous assumptions note that for next iteration 3 particles are picked from random process and only one (30%) of M is from old pool ie., P1. Proceed next iteration with this resampled pool of M particles!

## Slide 23: Monte Carlo Based Localization Particle Filter Approach
Initialize
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
Initialize M Particles Pi with uniform belief
Move each Pi based on robot motion model
Compare predicted sensor reading Z expected with actual sensor reading Z measured
Optionally filter out surprising measurements
Weigh each Pi based on importance weights
Resample for particle set for next iteration based on Darwinian approach augmented with short term vs long term likelihood ratio
Reset the belief of particles with equal likelihood

## Slide 24: Monte Carlo Based Localization Mixture(Dual) MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m, Φ = 0.25
Predict
Correct
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | P1 | P2 | P3 | P4
 | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
Important Note :The picture with algorithm is a variation of standard Mixture MCL for reference but the given numerical problem is a flavor of vanilla Mixture MCL.

## Slide 25: Monte Carlo Based Localization Mixture(Dual) MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m, Φ = 0.25
Predict
Correct
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
 | P1 | P2 | P3 | P4
 | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
(modified for simplicity)
+
Linear Regression Model = +1
P1 is drawn from the distribution of sensor measurement! Since P1will not be affected by motion model due to swap of role, its (x,y…) values remain same.

## Slide 26: Monte Carlo Based Localization Mixture(Dual) MCL Algorithm
 | P1 | P2 | P3 | P4
Pose | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | ~4.95 | 2.24 | 3 | 2.24
 | P1 | P2 | P3 | P4
 | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | ~4.95 | 2.24 | 3 | 2.24
(modified for simplicity)
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m, Φ = 0.25
Predict
Correct
Preprocess
Weigh
Resample
Repeat
Ze is measured using this form as usual.
But for P1 alternatively you may redesign a motion model based estimator like
this to determine Ze,1

## Slide 27: Monte Carlo Based Localization Mixture(Dual) MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m, Φ = 0.25
Predict
Correct
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | ~4.95 | 2.24 | 3 | 2.24
 | ~0.995 | 0.0005 | 0.018 | 0.0005
 | P1 | P2 | P3 | P4
 | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | ~4.95 | 2.24 | 3 | 2.24
 | ~0.995 | 0.0005 | 0.018 | 0.0005
(modified for simplicity)

## Slide 28: Monte Carlo Based Localization Mixture(Dual) MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m, Φ = 0.25
Predict
Correct
Preprocess
Weigh (Not efficient in pooling diverse particles in next iteration. Assumed that P1 uses Ze for W1 update)
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | ~4.95 | 2.24 | 3 | 2.24
 | ~0.995 | 0.0005 | 0.018 | 0.0005
Bel( | 0.9813 | 0.0005 | 0.0178 | 0.0005
 | P1 | P2 | P3 | P4
 | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | ~4.95 | 2.24 | 3 | 2.24
 | ~0.995 | 0.0005 | 0.018 | 0.0005
 | 0.9813 | 0.0005 | 0.0178 | 0.0005
(modified for simplicity)

## Slide 29: Monte Carlo Based Localization Mixture(Dual) MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m, Φ = 0.25
Predict
Correct
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | ~4.95 | 2.24 | 3 | 2.24
 | ~0.995 | 0.0005 | 0.018 | 0.0005
Bel( | 0.9813 | 0.0005 | 0.0178 | 0.0005
 | P1 | P2 | P3 | P4
 | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | ~4.95 | 2.24 | 3 | 2.24
 | ~0.995 | 0.0005 | 0.018 | 0.0005
 | 0.9813 | 0.0005 | 0.0178 | 0.0005
 | P1 | P2 | P3 | P4
 | (0.5, 0.5, 0) | (4,1,0) | (0.5, 0.5, 0) | (0.5, 0.5, 0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | P1 | P2 | P3 | P4
 | (0.5, 0.5, 0) | (4,1,0) | (0.5, 0.5, 0) | (0.5, 0.5, 0)
 | 0.25 | 0.25 | 0.25 | 0.25
One Naïve Estimation Model :
Average of Particles = (1.4,0.6,0)
Observe : Though the mixture model is able to handle noisy motion model from influencing the M, due to high Wi of Sensor model based particle P1, its not efficient in pooling diverse particles in next iteration if roulette wheel based mechanism is used.
Solutions: Use AIML to determine the balance between exploration vs exploitation OR use traditional Augmented MCL technique OR use Mixture model ratio to pool for next iteration!! 

## Slide 30: Monte Carlo Based Localization Idea 2: (Augmented)Mixture(Dual) MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m, Φ = 0.25
Predict
Correct
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | ~4.95 | 2.24 | 3 | 2.24
 | 0.995 | 0.0005 | 0.018 | 0.0005
Bel( | 0.9813 | 0.0005 | 0.0178 | 0.0005
 | P1 | P2 | P3 | P4
 | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | ~4.95 | 2.24 | 3 | 2.24
 | 0.995 | 0.0005 | 0.018 | 0.0005
 | 0.9813 | 0.0005 | 0.0178 | 0.0005
= = ~0.2535
= (1- α fast) +
= (1- α slow) +
= (1-0.5) (0.5)+
= ~0.38
= (1-0.1) (0.9)+
= ~0.84
= = ~0.45
MAX{0, (1-0.45)} = ~0.55
Hence for M=4 number of particle selection in next round with 0.6 probability (approx. to 60% only for this slide’s example), exploration proceeds and for rest exploitation is preferred
Resampling Effect : Approx. 40% of Particles are Informative. Retain them . Need randomization for other 60% of M particles!
One Naïve Estimation Model :
Average of Particles = (1.4,0.6,0)

## Slide 31: Monte Carlo Based Localization Idea 2: (Augmented)Mixture(Dual) MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m, Φ = 0.25
Predict
Correct
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | ~4.95 | 2.24 | 3 | 2.24
 | 0.995 | 0.0005 | 0.018 | 0.0005
Bel( | 0.9813 | 0.0005 | 0.0178 | 0.0005
 | P1 | P2 | P3 | P4
 | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | ~4.95 | 2.24 | 3 | 2.24
 | 0.995 | 0.0005 | 0.018 | 0.0005
 | 0.9813 | 0.0005 | 0.0178 | 0.0005
One Naïve Estimation Model :
Average of Particles = (2.75,1.5,0)
Resampling Effect : Approx. 40% of Particles are Informative. Retain them . Resample 2 particles using roulette tech from existing pool (red colored)
Need randomization for other 60% of M particles! Ie. Approx 2 particles(green colored)
 | P1 | P2 | P3 | P4
 | (0.5, 0.5, 0) | (4,5,0) | (0.5, 0.5, 0) | (6,0,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | P1 | P2 | P3 | P4
 | (0.5, 0.5, 0) | (4,5,0) | (0.5, 0.5, 0) | (6,0,0)
 | 0.25 | 0.25 | 0.25 | 0.25

## Slide 32: Monte Carlo Based Localization Idea 3: Mixture(Dual) MCL Algorithm
Initialize : M=4, 2D, 5X5, L(4.4), Move 1m east, Sensor noise = 0.5, Z m = 5m, Φ = 0.25
Predict
Correct
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3 | P4
Pose | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | ~4.95 | 2.24 | 3 | 2.24
 | 0.995 | 0.0005 | 0.018 | 0.0005
Bel( | 0.9813 | 0.0005 | 0.0178 | 0.0005
 | P1 | P2 | P3 | P4
 | (0.5, 0.5, 0) | (2,2,0) | (3,1,0) | (1,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25
 | (0.5, 0.5, 0) | (3,2,0) | (4,1,0) | (2,3,0)
Z e | ~4.95 | 2.24 | 3 | 2.24
 | 0.995 | 0.0005 | 0.018 | 0.0005
 | 0.9813 | 0.0005 | 0.0178 | 0.0005
One Naïve Estimation Model :
Average of Particles = (2.63,1.38,0)
Resampling Effect Sample 25% of next iteration particles from sensor model pool. Resample 1 particle using roulette wheel (if many particles like P1 are available) ie., P1 (red colored)
Sample 75% of next iteration particles from motion model Resample 3 particle using roulette wheel ie., P2,3,4 (green colored) . Here old P3 is selected twice and old P4 is selected once.
 | P1 | P2 | P3 | P4
 | (0.5, 0.5, 0) | (4,1,0) | (4,1,0) | (2,3,0)
Bel( | 0.25 | 0.25 | 0.25 | 0.25
 | P1 | P2 | P3 | P4
 | (0.5, 0.5, 0) | (4,1,0) | (4,1,0) | (2,3,0)
 | 0.25 | 0.25 | 0.25 | 0.25

## Slide 33: Monte Carlo Based Localization Particle Filter Approach
Initialize
Predict
Correct
Preprocess
Weigh
Resample
Repeat
Initialize M Particles Pi with uniform belief
Move each Pi based on robot motion model
Compare predicted sensor reading Z expected with actual sensor reading Z measured
Optionally filter out surprising measurements
Weigh each Pi based on importance weights
Resample for particle set for next iteration based on Darwinian approach augmented with short term vs long term likelihood ratio
Reset the belief of particles with equal likelihood

## Slide 34: Monte Carlo Based Localization MCL Algorithm
Initialize : M=3, 1D, 5X5, L(3 & 6), Move 1m east, ﬡ= 0.5, Z m = 0.5m
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3
Pose | -1 | 0 | 2
Bel( | 1/3 | 1/3 | 1/3
 | P1 | P2 | P3
 | -1 | 0 | 2
 | 1/3 | 1/3 | 1/3

## Slide 35: Monte Carlo Based Localization MCL Algorithm
Initialize : M=3, 1D, 5X5, L(3 & 6), Move 1m east, ﬡ= 0.5, Z m = 0.5m
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3
Pose | 0 | 1 | 3
Bel( | 1/3 | 1/3 | 1/3
 | P1 | P2 | P3
 | 0 | 1 | 3
 | 1/3 | 1/3 | 1/3
(modified for simplicity)
+
Linear Regression Model = +1

## Slide 36: Monte Carlo Based Localization MCL Algorithm
Initialize : M=3, 1D, 5X5, L(3 & 6), Move 1m east, ﬡ= 0.5, Z m = 0.5m
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3
Pose | 0 | 1 | 3
Bel( | 1/3 | 1/3 | 1/3
Z e | 3 | 2 | 3
 | P1 | P2 | P3
 | 0 | 1 | 3
 | 1/3 | 1/3 | 1/3
Z e | 3 | 2 | 3
Used Manhattan Distance
Restricted view measured w.r.t 2nd landmark from P3

## Slide 37: Monte Carlo Based Localization MCL Algorithm
Initialize : M=3, 1D, 5X5, L(3 & 6), Move 1m east, ﬡ= 0.5, Z m = 0.5m
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3
Pose | 0 | 1 | 3
Bel( | 1/3 | 1/3 | 1/3
Z e | 3 | 2 | 3
May be | Short | Short | Short
 | P1 | P2 | P3
 | 0 | 1 | 3
 | 1/3 | 1/3 | 1/3
Z e | 3 | 2 | 3
May be | Short | Short | Short
 | Mixture weights P(C ) | Measurement Likelihood P(Z=0.5 ¦ C) | 
Hit | 0.8 | 0.01 | Z m = Z e
Short | 0.1 | 0.95 | Z m < Z e
Max | 0.05 | 0.01 | Z m = Max
Rand | 0.05 | 0.2 | Others

## Slide 38: Monte Carlo Based Localization MCL Algorithm
Initialize : M=3, 1D, 5X5, L(3 & 6), Move 1m east, ﬡ= 0.5, Z m = 0.5m
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3
Pose | 0 | 1 | 3
Bel( | 1/3 | 1/3 | 1/3
Z e | 3 | 2 | 3
May be | Short | Short | Short
P(C short ¦Z m ) | 0.1*0.95*0.33 | ~0.0314 | ~0.0314
 | P1 | P2 | P3
 | 0 | 1 | 3
 | 1/3 | 1/3 | 1/3
Z e | 3 | 2 | 3
May be | Short | Short | Short
P(C short ¦Z m ) | 0.1*0.95*0.33 | ~0.0314 | ~0.0314
 | Mixture weights P(C ) | Measurement Likelihood P(Z=0.5 ¦ C) | 
Hit | 0.8 | 0.01 | Z m = Z e
Short | 0.1 | 0.95 | Z m < Z e
Max | 0.05 | 0.01 | Z m = Max
Rand | 0.05 | 0.2 | Others

## Slide 39: Monte Carlo Based Localization MCL Algorithm
Initialize : M=3, 1D, 5X5, L(3 & 6), Move 1m east, ﬡ= 0.5, Z m = 0.5m
Predict : Motion Update
Correct : Measurement Update
Preprocess
Weigh
Resample
Repeat
 | P1 | P2 | P3
Pose | 0 | 1 | 3
Bel( | 1/3 | 1/3 | 1/3
Z e | 3 | 2 | 3
May be | Short | Short | Short
P(C short ¦Z m ) | 0.1*0.95*0.33 | ~0.0314 | ~0.0314
 | P1 | P2 | P3
 | 0 | 1 | 3
 | 1/3 | 1/3 | 1/3
Z e | 3 | 2 | 3
May be | Short | Short | Short
P(C short ¦Z m ) | 0.1*0.95*0.33 | ~0.0314 | ~0.0314
 | Mixture weights P(C ) | Measurement Likelihood P(Z=0.5 ¦ C) | 
Hit | 0.8 | 0.01 | Z m = Z e
Short | 0.1 | 0.95 | Z m < Z e
Max | 0.05 | 0.01 | Z m = Max
Rand | 0.05 | 0.2 | Others
p = ~0.09
q = Denominator = ~0.11
p/q = ~0.84
p/q > ﬡ
Inference :
Reject the Z m . Z. Stop this iteration. No resampling .
Use the same particles again to begin next iteration.

## Slide 40: Monte Carlo Based Localization Particle Filter Approach
Initialize
Predict
Correct
Preprocess
Weigh
Resample
Repeat
Initialize M Particles Pi with uniform belief
Move each Pi based on robot motion model
Compare predicted sensor reading Z expected with actual sensor reading Z measured
Optionally filter out surprising measurements
Weigh each Pi based on importance weights
Resample for particle set for next iteration based on Darwinian approach augmented with short term vs long term likelihood ratio
Reset the belief of particles with equal likelihood
CAN BE APPLIED TO GRID BASED LOCALIZATION AS WELL WITH CAREFUL CUSTOMIZATION

## Slide 41: Required Reading T1 Chapter 4.2: 4.2.1, 4.2.2, 4.2.4, 8.3: 8.31, 8.3.2, 8.3.3, 8.3.4, 8.4
Next Class Plan :
Mapping
Occupancy Grid Mapping